## Slide 1: Experiment 4 : Thermistor Interface with Arduino

## Slide 2: Thermistor
  The word “Thermistor” is a combination of the words “Thermal” and “resistor“. A thermistor is a type of resistor whose resistance changes with the change in temperature.
  It is a passive component that does not require an extra power source to operate.
  They are inexpensive and easy accessible.
There are two types of thermistors:
PTC (Positive Temperature Coefficient) Thermistor
NTC (Negative Temperature Coefficient) Thermistor

## Slide 3: POSITIVE TEMPERATURE COEFFICIENT (PTC)THERMISTOR
  PTC or Positive Temperature Coefficient thermistor resistance is directly proportional to the surrounding temperature.
  Its resistance increases with an increase in the temperature and decreases with a decrease in the temperature.

## Slide 4: NEGATIVE TEMPERATURE COEFFICIENT (NTC)THERMISTOR
  NTC or Negative temperature coefficient thermistor has a negative coefficient k. therefore, its resistance varies inversely with the temperature.
  The resistance decreases with an increase in temperature and vice versa

## Slide 5: Thermistor

## Slide 6
In experiment 1, 2 & 3, we have learned
  How to use pinMode command
  How to use digitalWrite command
  How to declare variables using int, define
  How to use digitalRead command
  How to do serial communication
  How to use analogWrite command
  How to use analogRead command
In experiment 4, we are going to learn
  How to use mathematical formulae
  How to use If, elseif, for loop statements.
  How to declare variables using float

## Slide 7: Aim
The main objective of this experiment is
  To interface thermistor with Arduino UNO, to read thermistor data and print on the Serial Monitor.
  To turn on LED if temperature is more than 30 oC.
  To turn off both LED1, LED2 if temperature is less than 85 oF, to turn on LED1 if temperature is between 85 oF to 95 oF, and to turn on both LED1, LED2 if temperature is more than 95 oF.

## Slide 8: Circuit Connections: Objective 4(a)

## Slide 9: Value Convertions

## Slide 10
where
T is the temperature (in kelvins),
R2 is the resistance at T (in ),
C1, C2, C3 are Steinhart–Hart coefficients, which vary depending on the type and model of thermistor and the temperature range of interest.
Steinhart–Hart Equation
Kelvin to Celsius Temperature Convertion
Value Convertions
Celsius to Fahrenheit Temperature Convertion

## Slide 11: Program: Objective 4(a)
float Vo = 0;
float R1 = 10000;
float R2, T_Kelvin, T_Celsius, T_Fahrenheit;
float c1 = 1.009249522e-03;
float c2 = 2.378405444e-04;
float c3 = 2.019202697e-07;
void setup()
{
Serial.begin(9600);
}
void loop()
{
Vo = analogRead(A1);
R2 = R1 * ((1023.0 / Vo) - 1.0);
T_Kelvin=(1.0/(c1+c2*log(R2)+c3*log(R2)*log(R2)*log(R2)));
T_Celsius = T_Kelvin - 273.15;
T_Fahrenheit = (T_Celsius * 9.0)/ 5.0 + 32.0;
Serial.print("Resistance: ");
Serial.print(R2);
Serial.println(" Ohms");
Serial.print("Temperature: ");
Serial.print(T_Kelvin);
Serial.println(" Kelvin");
Serial.print("Temperature: ");
Serial.print(T_Celsius);
Serial.println(" Celsius");
Serial.print("Temperature: ");
Serial.print(T_Fahrenheit);
Serial.println(" Fahrenheit");
delay(2000);
}

## Slide 12: Circuit Connections: Objective 4(b)

## Slide 13: Objective 2
float Vo = 0;
float R1 = 10000;
float R2, T_Kelvin, T_Celsius, T_Fahrenheit;
float c1 = 1.009249522e-03;
float c2 = 2.378405444e-04;
float c3 = 2.019202697e-07;
void setup()
{
Serial.begin(9600);
pinMode(13,OUTPUT);
}
void loop()
{
Vo = analogRead(A1);
R2 = R1 * ((1023.0 / Vo) - 1.0);
T_Kelvin = (1.0/(c1+c2*log(R2)+c3*log(R2)*log(R2)*log(R2)));
T_Celsius = T_Kelvin - 273.15;
T_Fahrenheit = (T_Celsius * 9.0)/ 5.0 + 32.0;
Serial.print("Resistance: ");
Serial.print(R2);
Serial.println(" Ohms");
Serial.print("Temperature: ");
Serial.print(T_Kelvin);
Serial.println(" Kelvin");
Serial.print("Temperature: ");
Serial.print(T_Celsius);
Serial.println(" Celsius");
Serial.print("Temperature: ");
Serial.print(T_Fahrenheit);
Serial.println(" Fahrenheit");
if (T_Celsius>=30)
{
digitalWrite(13,HIGH);
delay(1000);
}
delay(1000);
}

## Slide 14: Circuit Connections: Objective 4(c)

## Slide 15
float V0=0;
float R1 = 10000;
float RT;
float T_Kelvin, T_Celsius;
float T_Fahrenheit;
float c1=1.009249522e-03;
float c2=2.378405444e-04;
float c3=2.019202697e-07;
void setup()
{
Serial.begin(9600);
pinMode(13,OUTPUT);
pinMode(7,OUTPUT);
}
void loop()
{
Serial.print(" Thermal Resistance:");
Serial.print(RT);
Serial.println(" Ohms");
Serial.println(" Temparature:");
Serial.print(T_Kelvin);
Serial.println(" kelvin");
Serial.print(" Temparature:");
Serial.print(T_Celsius);
Serial.println(" celsius");
Serial.print("Temparature:");
Serial.print(T_Fahrenheit);
Serial.println(" Fahrenheit");
delay(1000);
}
V0=analogRead(A0);
RT = R1*((1023.0/V0) -1.0);
T_Kelvin = (1.0/(c1+c2*log(RT)+c3*log(RT)*log(RT)*log(RT)));
T_Celsius=T_Kelvin-273.15;
T_Fahrenheit=(T_Celsius*9.0)/5.0+32.0;
if(T_Fahrenheit<=95)
{ digitalWrite(13,LOW);
digitalWrite(7,LOW);
delay(1000);
}
else if(T_Fahrenheit>=95 && T_Fahrenheit<=99)
{
digitalWrite(13,HIGH);
digitalWrite(7,LOW);
delay(1000);
}
else
{
digitalWrite(13,HIGH);
digitalWrite(7,HIGH);
delay(1000);
}

## Slide 16: Self Assessment Questions
What is a thermistor?
How can we convert the analog reading from the thermistor into temperature values?
What is the purpose of the resistor connected in the circuit with the thermistor?
What are some applications of temperature measurement using a thermistor and Arduino UNO?

## Slide 17
THANK YOU
Team – Fundamentals of IoT & Sensors